## Slide 1: Fiber Optic Communications
Lecture 4
Stephen E. Ralph
Fiber Modes
Multimode Fiber
Spring 2026
Vg
Vph

## Slide 2: Homework Due Wednesday 4 Feb 2026
Review basic E&M, Chapter 1 Kumar and Deen
Plane waves, relationships between wavelength, velocity, k-vector
Phase and group velocity, physical meaning and mathematical definition
Read Chapter 2 and 3 Kumar and Deen
Read Journal articles
Fiber-optic transmission and networking: the previous 20 and the next 20 years,
  P. J. Winzer, D. T. Neilson, and A. R. Chraplyvy
Future Optical Networks
  Michael J. O’Mahony, Christina Politi, Dimitrios Klonidis, Reza Nejabati, and Dimitra Simeonidou, JLT V24, 2006

## Slide 3
Kumar and Deen Problems 1.9,
Kumar and Deen 1.15
Pulse Propagation
Compute and plot the temporal shape and spectral content of a single optical pulse. Assume the carrier is essentially monochromatic at center wavelength 1552nm (plot both amplitude and phase, use a frequency axis centered on the carrier and denote frequency offset from carrier in units of GHz). The pulse should have the following characteristics:
  a) Single raised cosine pulse with pulse width corresponding to 32 Gbps, and excess bandwidth factor of 0.1. The FWHM should be = symbol slot T.
  b) Roughly estimate the temporal spread of the pulse after 10km and 100km in standard fiber. (Suggestion: estimate fto be =1/T).
  c) The pulse in part a) after propagating through 10km and 100km of standard fiber. Neglect loss (=0) and nonlinear (intensity dependent) effects. Plot the temporal shape. Indicate both real time units (ps) and a bit slot unit. Choose a time scale appropriate for the anticipated temporal spread i.e. at least 10ns for the 1000km case. You also need sufficient temporal resolution, at least 20points in the original pulse shape or ~1ps.
  Also plot the phase in the frequency domain. Show only the quadratic phase behavior (i.e. remove any linear phase behavior). Be sure to unwrap any phase discontinuities.

## Slide 4
4) A Gaussian pulse (100ps FWHM) is launched into 80km of SSMF fiber with initial power of +15 dBm. The central wavelength of the pulse is 1550nm. State clearly any assumptions.
  a) If you measure the power at the end of the fiber, what value are you likely to observe? (Answer both in mW and dBm)
  b) What is the loss parameter a?
  c) What is the pulse width (FWHM) at the end of the fiber?
  d) At the input to the fiber what is the spectral content ( FWHM ) if the pulse initially unchirped?
  e) At the output of the fiber the pulse is chirped. Is it positively or negatively chirped? Does this mean the “blues” are ahead of or behind the “reds”? What is the spectral content ( FWHM )?
  f) What is the value of the chirp parameter at the output of the fiber? Write an expression for the pulse shape which includes the chirp parameter.

## Slide 5: Waves Summary
Known as the dispersion relation, i.e. how k (space) relates to w (time)
Solution
Examination of constant phase of the argument of the cosine solution yields the phase velocity
Phase velocity in vacuum
Wave Equation(1D case)
where
Examination of the cosine solution in the wave equation shows
Thus
3D with E = E eiwt

## Slide 6: Electromagnetic Modes
Confined structures: Waveguide Modes
  For waveguides, the stable condition for a mode requires that the shape of the complex amplitude profile in the transverse dimensions remains exactly constant
  For metal waveguides the E-field must be zero at the metal boundary
MODES: Stable electric field distributions in waveguides, optical resonators or in free space that satisfy Maxwell’s equations and boundary conditions
Metal Waveguide
WAVEGUIDE MODES: Solution of the wave equation that satisfies the boundary conditions and has a spatial distribution does not change with propagation
Normal E-field starts and terminates with charge
Tangential E-field is zero at conductor

## Slide 7: Mode Classification
Transverse electromagnetic (TEM) modes
  Neither electric nor magnetic field in the direction of propagation
Transverse electric (TE) modes
  No electric field in the direction of propagation. These are sometimes called H modes because there is only a magnetic field along the direction of propagation (H is the conventional symbol for magnetic field)
Transverse magnetic (TM) modes
  No magnetic field in the direction of propagation. These are sometimes called E modes because there is only an electric field along the direction of propagation
Hybrid modes
  Non-zero electric and magnetic fields in the direction of propagation
Rectangular transverse mode patterns TEM(mn)

## Slide 8: Electromagnetic Modes
Confined structures: Waveguide Modes
  For waveguides, the stable condition for a mode requires that the shape of the complex amplitude profile in the transverse dimensions remains exactly constant
  For metal waveguides the E-field must be zero at the metal boundary
Metal Waveguide
MODES: Stable electric field distributions in waveguides, optical resonators or in free space that satisfy Maxwell’s equations and boundary conditions
WAVEGUIDE MODES: Solution of the wave equation that satisfies the boundary conditions and has a spatial distribution does not change with propagation

## Slide 9: Electromagnetic Modes
Confined structures: Waveguide Modes
  For dielectric waveguides, like glass optical fiber, the field and energy exists in the cladding
  For cylindrical dielectric waveguides the modes are described by Bessel functions
  The lowest order mode is approximately Gaussian
  A waveguide has only a finite number of guided propagation modes for a specified wavelength, the intensity distributions have a finite extent around the waveguide core
Dielectric Waveguide
MODES: Stable electric field distributions in waveguides, optical resonators or in free space that satisfy Maxwell’s equations and boundary conditions
WAVEGUIDE MODES: Solution of the wave equation that satisfies the boundary conditions and has a spatial distribution does not change with propagation

## Slide 10: Electromagnetic Modes
Dielectric Waveguide
MODES: Stable electric field distributions in waveguides, optical resonators or in free space that satisfy Maxwell’s equations and boundary conditions
Confined structures: Waveguide Modes
  For cylindrical dielectric waveguides the modes are described by Bessel functions, however the lowest order mode is nearly Gaussian
  A waveguide supports only a finite number of guided propagation modes for a specified wavelength and waveguide size
Note: Free-space also has stable modes including plane Waves and Gaussian beams

## Slide 11: Transverse Resonance Condition
The transverse resonance condition is an analytical technique used to determine the propagation constants and mode conditions in waveguides
TRC: For a mode to exist, the total round‑trip phase shift in the transverse direction must equal an integer multiple of 2π
  This restricts the allowed values of kx and hence only discrete values of b are allowed
  The TRC is also a dispersion relation
  Note f are sometimes written as -2F
Phase shift for passing through core
Phase shift due to TIR at core-cladding interface
Phase shift due to TIR at core-cladding interface
k = kx
n1k0
b
The effects of the boundary conditions may be viewed as a requirement on the roundtrip phase across the waveguide
A guided wave must form a self‑consistent standing wave pattern in the transverse direction (perpendicular to propagation)
In the ray picture the wave accumulates phase as it travels across the core
It also acquires additional phase shifts upon reflection at the cladding boundaries

## Slide 12: Types of Fiber: Core Size
Waveguides support modes that satisfy the EM boundary conditions between the core and cladding
Very small cores only support one transverse mode (even the smallest core supports at least one mode)
Larger cores support many transverse optical modes that exhibit different (more complex) intensity profiles
Ray Picture
Intensity Profiles
Multimode Fiber
Single Mode Fiber
Lowest order Mode
Index contrast
Δ ≈ 0.01 to 0.02
Core n1= ~1.450
Cladding n2= ~1.444
Δ ≈ 0.0036 to 0.004
Core n1= ~1.480-1.500
Cladding n2= ~1.444
Δ ≈ 0.01 to 0.03

## Slide 13: Mode Size vs. Wavelength
For low frequencies (large l) the mode is spatially large and extends significantly into the cladding thus the effective index is very close to that of the cladding n2
For high frequencies (short l) the mode is spatially confined mostly to the core thus the effective index is very close to that of the core n1
l=1320nm
l=1550nm
l=1650nm
core
n2
n1
For a given mode, the distribution of field (and power) changes with wavelength

## Slide 14: Dispersion b vs w
n2 < n1
w
b
b = n2 w/c
Radiation modes
For low frequencies (large l) the mode is spatially large and extends significantly into the cladding thus the effective index is very close to that of the cladding n2
For high frequencies (short l) the mode is spatially confined to the core thus the effective index is very close to that of the core n1
b(w)
b = n1 w/c
Knowledge of b(w) is required to understand signal propagation
n1 and n2 are functions of w
In the figure we neglect this dependence

## Slide 15
Fiber Modes

## Slide 16: Fiber Modes and Waveguide Dispersion (summary)
For a given mode, the group velocity depends on the wavelength (even if the material dispersion is negligible)
  The precise mode field distribution changes slightly when the wavelength changes
  The relative fraction of the electric field in the core versus cladding changes
  Thus the effective index changes and the group velocity must change
We need to determine the mode field profile and b(w) in fibers
  The solution is analytic for step index fibers but is typically solved numerically
  We start with the wave equation (Helmholtz equation) in cylindrical coordinates
  The 3D wave equation
  becomes:
We have written just the axial component Ez, there are of course six variables Ez, Er, Ef and Hz, Hr, Hf , but only two are independent
The frequency dependence is not explicitly written
ko = 2p/lo
Equivalent to Keiser Eq 2.36

## Slide 17: Optical Fiber Modes
The optical fiber has a circular waveguide
Solve Maxwell’s equations with cylindrical symmetry
Solutions vary with radius r and angle f
  Fields in the core are non-decaying
  Fields in the core have a r as
    J, Y Bessel functions of the first and second kind
  Fields in the cladding are decaying
    A boundary condition is E0 as r
    K modified Bessel functions of second kind
    In a rectangular system the fields decay exponentially
There are two mode number to specify each distinct mode
  n is the radial mode number or mode index
  m is the angular mode number or azimuthal mode index

## Slide 18: Finding the Solution
Separation of variables suggests
Resulting in 3 separate equations (ODEs), one for each variable
Equation for r dependence has Bessel function solutions
J, Y, K and I, are types of Bessel functions and A, A’, C, and C’ are constants
b is a separation constant
m2 is a separation constant
Keiser’s q2
Equivalent to Keiser Eq 2.38
Z dependence is identical to plane wave
f dependence is periodic in f
The solutions to this are Bessel functions
(note: n here is index of refraction)

## Slide 19: Solution
In the core the propagation constant b is related to the free space wavevector:
In the cladding the evanescent decay constant
Boundary conditions (field must be finite and go to zero as r->∞ )
Similar relationships exist for Hz
Using Maxwell’s Equations, expressions can be determined for, Er, Ef and, Hr, Hf in terms of Ez and Hz
k
n1k0
b
g
n2k0
b

## Slide 20: Eigenvalue Equation for b
Using the boundary conditions for continuous tangential E and H across the core-cladding interface gives four equations for continuity of Ez, Ef, Hz, and Hf
These four equations have solution when the determinant of the corresponding matrix is zero, yielding:
This provides a method to determine b for any given set of ko, a, n1 and n2
There are multiple solutions for each azimuthal mode index m, m = 0, 1, 2, 3…
The solutions are identified in terms of m and n and bmn
  Where n is the radial mode index, n = 1, 2, 3 ….
In general Ez and Hz are both non zero except for m = 0
We therefore call these hybrid modes designated HEmn and EHmn depending on whether Hz is > Ez or not
For m=0 we do have TE0n and TM0n
Keiser 2.54

## Slide 21: Bessel Functions
1st kind
2nd kind
Modified Bessel functions: Iα, Kα special case with purely imaginary argument
Bessel functions of the first kind: Jα
Bessel functions of the second kind : Yα

## Slide 22: Ray Picture
A meridional ray has no φ component –it passes through the z axis
Ray propagation with a component in the φ direction, is called a skew ray
Skew rays exhibit a spiral-like path down the core, never crossing the z axis
(n1k0)2= βr2+ βφ2+ β2= βt2+ β2
TE (Ez= 0) and TM(Hz= 0) modes are possible
  These modes correspond to meridional rays and pass through the fiber axis
We refer to these modes as TElm and TMlm modes
  Two indices to describe the two degrees of freedom

## Slide 23: Hybrid Modes
Hybrid modes: both Ez and Hz are nonzero
  These are skew rays (helical path without passing through the fiber axis)
The modes are written as HElm and EHlm depending on whether the components of H or E make the larger contribution to the transverse field
The full set of circular optical fiber modes therefore comprises: TE, TM (meridional rays), HE and EH (skew rays) modes

## Slide 24: Effective Index and V Number
D = (n1-n2)/n1
And normalized propagation constant b:
The behavior of b vs. V depicts the fiber mode structure
  When TE01 and TM01 modes reach cutoff then the fiber is single mode
  This is equivalent to Jo(V)=0
  or V < 2.405
HE11 is a hybrid mode and it has the lowest cutoff (at V=0), i.e. does not cutoff
Each mode is uniquely characterized by a specific b(w)
  We can therefore define a mode index of refraction (mode index)
  The mode propagates with the effective index constrained by the core and cladding indices:
  The mode reaches cutoff when g=0 or
We also define a normalized frequency V
Approx V for SSMF

## Slide 25: Waveguide Dispersion
Waveguide dispersion is generally the smallest contributor to the total dispersion
  It can dominate near the dispersion minimum i.e. l=1300nm for single mode waveguide
  It must be included since it typically shifts the dispersion dominated by material dispersion
Waveguide dispersion: wave vector varies with wavelength
In order to determine waveguide dispersion we must return to the eigenvalue equation which defines the allowed modes
  The EV equation was written in terms of the transverse wavevector k
  The transverse wavevector depends on:
When the wavelength changes, ko changes and hence the propagation constant b must change
k is fixed for a particular mode, it is a solution to the EV equation
The mode shape stays essentially the same when the wavelength changes [we are assuming that the wavelength changes are small, consistent with that needed to support data streams]

## Slide 26: Weakly Guided modes
For telecom Special case of cylindrical modes
Typical of all common optical fibers index contrast is low fibers Δ<< 1
  Weakly guided modes n1~ n2, determinant equation simplifies, modes become degenerate
  Ez and Hz are both nearly zero
  Designated LP modes for Linearly Polarized
The propagation is preferentially along the fiber axis and the field is predominantly transverse
Modes are approximated by two linearly polarized components
  both Ez and Hz are approximately zero)

## Slide 27: Fiber LP modes
Relation between the LP modes and the “real” exact waveguide modes HE11x, HE11y, TE01, TM01, HE21a, and HE21b of the six-mode FMF

## Slide 28: LP modes: Normalized Propagation Constant
Fig 2.16 Kumar and Deen

## Slide 29: Intensity profiles for the lowest LP modes
Two polarizations each

## Slide 30: Gaussian Approximation for the LP01mode
FIG. 8 Citation D. Marcuse, "Gaussian approximation of the fundamental modes of graded-index fibers," J. Opt. Soc. Am. 68, 103-109 (1978); https://www.osapublishing.org/josa/abstract.cfm?uri=josa-68-1-103
Fig. 2 Citation Vincent Trudel, Yves St-Amant, "One-dimensional single-mode fiber-optic displacement sensors for submillimeter measurements," Appl. Opt. 48, 4851-4857 (2009); https://www.osapublishing.org/ao/abstract.cfm?uri=ao-48-26-4851
The LP01 mode intensity varies with radius as J02(ur/a) inside the core and as K02(wr/a) in the cladding
  The resultant intensity profile closely fits a Gaussian function width w0, known as the mode-field radius defined as the radial distance from the core center to the 1/e2 point of the intensity profile
E(r) = E(0) exp (-r2 / w02)
I(r) = I(0) exp(-2r2/w02)

## Slide 31
More on Guided Modes

## Slide 32: Planar Guided Wave Structures
a) Slab waveguide b) strip waveguide c) rib waveguide
d) strip-loaded waveguide e) diffused waveguide f) rib-type SOI waveguide
buried oxide
Lower cladding
Waveguide core
Top cladding

## Slide 33: Coupling Between Adjacent Waveguides
Two adjacent optical modes exchange power
  Phase matching
  Spatial overlap
Directional coupler: no power is coupled into backward waves
3dB coupler: input power is equally split between two output guides

## Slide 34: Optical Couplers
2x2 couplers
  Waveguides are tapered, V number decreases, expanding evanescent field
  Controlling parameters
    Size of reduced waveguide, coupling region length, difference in waveguide size
Coupled mode theory allows a description of the wave transverse overlap
Relative phase of each input mode is critical to performance
Planar coupled waveguides
Fused biconical fiber coupler
Length determines coupling ratio

## Slide 35: Couplers
RF: microstrip
RF: metal waveguide
Optical: index guided

## Slide 36: Co-directional coupling
For coupling between the modes we need to add a dielectric perturbation to the wave equations
  Without the dielectric perturbation the situation is just two waves passing each other in a dielectric
  De2 acts as a perturbation for E1
  De1 acts as a perturbation for E2
The polarization perturbation is of the form

## Slide 37: Coupled mode theory; Two identical waveguides
Using the wave equation, we find added source terms which originate from both waveguides
  E(x,y,z)=A(z)E(x,y)
  A(z): complex field amplitude including a phase term e-jbz
  E(x,y): Field distribution in one waveguide
Couple Mode Equations
  b is the same for both waveguides (synchronous case)
Initial conditions
Solutions
driven waveguide lags 90° behind phase of driving waveguide
New source terms
k: Coupling coefficient

## Slide 38: Power Transfer: Synchronous case
Power Flow
  Periodic
Length needed to transfer all power from one waveguide to the other
Calculated power distribution along the length of the waveguide
When kz=p/2 all power is transferred

## Slide 39: Periodic Exchange of Power
In the absence of loss the power exchange continues indefinitely
Coupling between two modes is not symmetric, kum ≠ k*mn, unless bu = bm
For synchronous waveguides the coupling is complete
For asynchronous waveguides complete power transfer does not occur
For both cases the power transfer is periodic
Asynchronous case

## Slide 40: Optical Couplers
Couplers length depends on the need
  a) complete switching of power from one guide to the other
  b) splitting the power half and half i.e. a 3dB coupler
  Can also create other couplers 10%, 5% etc
  Dynamic coupler made by changing Db using electro-optic effect
NB: there is a relative phase change between the two outputs and the relative input phase matters
  This impacts how you cascade these devices

## Slide 41: Optical Signal Control: Scattering Matrix Representation
Optical Hybrids
E1,in
E2,in
E2,o
E1,o
Where k is the coupling coefficient
For k l = p/4 the device is a 3dB coupler
    Each term then has magnitude

## Slide 42: Optical Signal Control: Scattering Matrix Representation
Optical Hybrids
E1,in
E2,in
E2,o
E1,o